## Slide 1
Hash or Merge?
Adaptive GPU Acceleration for SpGEMM
Tengfei Xia, Yizhou Xue
Advisor: Zhihua Fan
State Key Laboratory of Processors, Institute of Computing Technology, CAS
University of Chinese Academy of Science
Notes: 各位评委老师，大家上午好，我是中国科学院计算技术研究所的范志华，接下来开始我的答辩汇报

## Slide 2
Background
Mainstream SpGEMM methods mainly adopt Merge-Based or Hash-Based accumulation
accumulation时间占比图
Merge-Based
Hash-Based
PPoPP 19/MICRO 20/ASPLOS 21/PACT 25
PPoPP 20/IEEE Access 22/ISCA 24/HPCA 25
Merge Accumulator
compare column IDs
sum duplicates
(1,2+7)
(2,5)
(3,6)
(4,4)
(1,2)
(4,3)
(1,7)
(3,6)
(2,5)
(4,1)
partial products: (column,value)
Output
(1,2)
(4,3)
(1,7)
(3,6)
(2,5)
(4,1)
partial products: (column,value)
(1,9)
(2,5)
(3,6)
(4,4)
Output
Hash Accumulator
slot
key
value
0
1
2
3
4
...
—
1
2
3
4
...
—
9
5
6
4
...
hash table (key: column ID)
insert (1,2) → slot 1
insert (4,3) → slot 4
insert (2,5) → slot 2
accumulate key 4 → 3+1=4
accumulate key 1 → 2+7=9
insert (3,6) → slot 3
Notes: 应用同时具有计算模式多样、数据并发度高和实时约束严格三个特征。但传统处理器的执行方式、算力组织相对固定，难以满足灵活性、高并发和实时性需求。因此，论文研究的核心问题是：如何解决复杂多变的高通量负载与相对固定的处理器架构之间的矛盾。
围绕这一问题,形成3个创新：在执行模型层让程序高效流动；在计算阵列层让算力灵活重组；在计算单元层使无效计算不再发生。三者共同构成负载自适应的高通量处理器

## Slide 3
Insight
Neither merge nor hash consistently performs best across all matrices
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 4
Design1: Adaptive Merge–Hash Workflow Dispatch
 Offline Threshold Choosing
 Overhead Hiding via Overlap
 CPU-side Online Dispatcher
CPU dispatcher uses learned thresholds to choose Merge or Hash with negligible overhead
training matrices
(disjoint from test set)
Profiling &
threshold search
Chosen thresholds: α, β, γ
公式列在这加粗
Input sparse matrix
CPU Dispatch Module
Feature extraction
n: matrix row number
: duplication/ fan-in indicator
flop: total arithmetic work
workload
selection
data
transfer
GPU compute
Time
CPU
dispatch
H2D
transfer
GPU
compute
Thresholds are learned offline from 1000 matrices unrelated to the 100 test matrices
CPU-side selection overlaps with transfer,hiding dispatch. GPU compute dominates afterward.
n > α
> β
OR
flop > γ
Merge
Merge
Hash
No
Yes
No
Yes
before accumulation
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 5
Design2: 。。。。的Merge
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 6
Design3: 。。。。的Hash
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 7
Design 4: Symmetry-Aware Adaptive Dispatch for AAT
Property: is symmetric about the main diagonal
 Symmetry Property
 GPU-side Adaptive Dispatch within Triangle
 Irregular Upper-Triangle
Opportunity: compute only the upper triangle,
Mirror to lower triangle
1
✖
A
AT
0
2
0
3
0
4
0
5
1
0
4
0
3
0
2
0
5
5
0
14
0
9
0
14
0
41
...
...
Upper triangle (by rows)
Row 0
Row 1
Row n
large scale
small scale
Observation: triangular rows naturally have different scales and numbers of nonzeros, from top to bottom
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 8
Evaluation
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 9
Conclusion
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利

## Slide 10
Engineering Optimizations
Notes: 第一项贡献面向执行模型。传统线程级数据流粒度过粗，面对非规则程序时，调度循环难以高效流水。论文选择指令块作为新的执行单位，系统构建激活、同步和访存语义及其计算微架构，在数据流灵活性与硬件执行效率之间取得平衡。相关成果包括Europar、APPT25、ISCA26和授权专利